## Slide 1: OpenFMB Specification Development Plan
M. Joe Zhou, Stuart Laval
Co-Chairs, NAESB OpenFMB TF
OpenFMB Task Force Update
May 13th, 2015
NAESB OpenFMB Task Force

## Slide 2: What is Open Field Message Bus?
Framework and reference architecture for Distributed Intelligence Apps and systems
  Cybersecurity, microgrids, DER, DA, AMI
  Blueprint for utility interoperability test beds
Standard API for Electric Grid interoperability
  Secure, peer-to-peer, multi-vendor, outside data center
Common Semantic models based on existing standards (CIM, IEC 61850)
Existing Internet of Things (IoT) publish-subscribe protocols (DDS, MQTT, AMQP, XMPP, CoAP, etc.)
Repository of adapters from utility protocols (Modbus, DNP3, C12, GOOSE/MMS)

## Slide 3: Guiding Principles
There is no “one size fits all” technology for interoperability between DERs and existing grid, so the OpenFMB framework should support multiple data model standards and communication protocols depending on the operational and functional requirements
Leverage what has been done before, no reinventing the wheels
Focus on business value and objectives in solving real world problems
Collaborate and coordinate with other relevant smart grid standards bodies, no duplication of effort and scope
Time to market is important to provide real solution and standard to the industry in order to enable field interoperability for on-going deployments
Flexibility, scalability and backwards compatibility (where feasible) are critical
Security and configuration should be built into the standard, not an afterthought.

## Slide 4: Introduction and Background
NAESB has been involved in the smart grid standards development
  PAP09 – Demand response use cases that led to OpenADR specification
  ESPI – Energy Service Provider Interface that led to Green Button.
NAESB, as an ANSI accredited SDO, typically files their standards with FERC and informs NARUC. This increases the exposure and possibilities of utility regulators adopting said standards.
OpenFMB task force will be a special purpose task force under the NAESB Retail Market Quadrant (RMQ).
OpenFMB TF will work closely with SGIP and UCAiug to facilitate the development, implementation, and future enhancements to the standard.

## Slide 5: Industry Drivers for OpenFMB
Rapid maturing and adoption of IoT Technologies in many industries
Renewable energy resources integration into the Grid – especially at the distribution and end consumer levels
The advent of Distribution Service Platform Provider (DSPP) role and the potential need to support Transactive Energy implementation.
Transition from top down power grid architecture into networked, two way power flow, and distributed supply and demand power network.
An open standard is needed to unlock the value of field devices and networks, and to enable distributed intelligence for more reliable and resilient grid of the future.

## Slide 6: OpenFMB Specification – The Key Components
Reference Architecture
Use Cases
Platform Independent Model (Semantic Model, Messages & Services)
Platform Specific Model (DDS, MQTT and Hybrid, etc.)
Implementation Guidelines

## Slide 7: OpenFMB – Reference Architecture
Duke Energy’s Distributed Intelligence Platform Reference Architecture Volume I: Vision Overview provides a great foundation for the standard development.
Task Force will need to review the work contributed by Duke, and discuss/decide how to leverage it, and what potential areas may require more work, such as:
  Security Architecture
  Node Classification
  Interaction Patterns
  Reference Architecture components – what is informative vs. what is normative for the standard
  Reference Model relative to other standards
Leverage similar work done from other IoT standards initiatives.
  http://www.iiconsortium.org/resource-hub.htm
  http://www.iot-a.eu/public

## Slide 8: OpenFMB – Reference Architecture
Key Development Focus within this Task Forse:
  Node Classification – consideration of a role/functional driven node model
  Integration interaction patterns:
    Logical patterns
    Mapping of logical patterns to physical protocols (DDS, MQTT, Web Services, etc.)
  Security design to support node classification and enable the integration patterns - both logical and physical.
The goals is to achieve both semantic and technical interoperability “as much as” it can.

## Slide 9: OpenFMB – Use Cases
Use Cases will drive the content of OpenFMB 1.0 Specification in terms of model, messages and services. We must decide a subset of use cases in the following categories to have a manageable scope.
Use Cases being developed under SGIP:
Include configuration and security requirements in the use cases.

## Slide 10: OpenFMB – Platform Independent Model
OpenFMB Semantic Model
IEC CIM
IEC 61850
IEEE
C37
IEEE
1588
DNP3
others

## Slide 11: OpenFMB – Platform Specific Model
OpenFMB
Protocol Specific Message/Services
DDS
CoAP
MQTT
REST
XMPP
......
AMQP

## Slide 12: OpenFMB – Implementation Guidelines
NAESB OpenFMB TF will develop implementation guidelines
NAESB will look to SGIP to provide framework and guidance on how this should be accomplished.
NAESB will look to UCAiug to setup an OpenFMB Users Group to help promote, implement, and provide testing and certification services. To be discussed further with SGIP and UCAiug.

## Slide 13: OpenFMB 1.0 - Deliverables
OpenFMB Reference Architecture Document
OpenFMB Platform Independent Model (semantic model) version 1.0 (UML, in support of the SGIP use case scope)
OpenFMB Platform Specific Model version 1.0 (XSD and IDL, in support of the SGIP use case scope)
OpenFMB Implementation Guidelines Document

## Slide 14: Timeline
Requirements
Design
Draft
Task Force Voting
30 Day Public Comment
30 Day Membership Ratification
NAESB Executive Committee Meeting on Feb. 2016
March - May
June - August
Sept.-Nov.
DistribuTECH 2016
Feb. 9-11 (Orlando, FL)
Dec.
Jan. – March
2015
2016
SGIP Engage 2015
(March 4, 2015)
OpenFMB Use Case Prioritization
(April 2, 2015)
OpenFMB TF
F2F Meeting #1 (May 15, 2015)
OpenFMB TF
F2F Meeting #2 (TBD)
OpenFMB TF
F2F Meeting #3 (TBD)

## Slide 15: OpenFMB Roadmap
New Use Cases
2015 – OpenFMB 1.0
2016 – 2017 OpenFMB 2.0
Expanded Models, Messages and Services
Expanded Models/Services and New Protocols
Enhancements
Enhancements

## Slide 16: Next Steps
We need broad participation in NAESB OpenFMB Task Force
  Bi-weekly calls, every other Fridays from 1-3pm Central (5/1, 5/15, 5/29, 6/12, 6/26, etc.)
  F2F meetings (TBD)
  Looking for resources who are able to spend time contributing to and/or reviewing the work products
We want to manage this to accomplish the goals by the end of this year, with a defined scope and project plan.
Key items to focus on in the next month:
  Reference Architecture (main topic for May 1st meeting)
  OpenFMB PIM Approach (how to leverage CIM and 61850, main topic for the May 15th meeting)